## Slide 1: D: Initial Uncertainty Analysis for Water and Energy Sectors
Robert Lempert, RAND
Nicholas Burger, RAND

## Slide 2: Outline
Rob describes:
  Range of climate data we are using in this study
  RDM analyses
  RDM analysis using WEAP model of climate impacts on Volta (and Orange-Senqu) basins
Nick describes:
  Energy robustness analysis

## Slide 3: Traditional Decision Methods Make Sense If We Don’t Face Much Uncertainty
When the future
  Isn’t changing fast
  Isn’t hard to predict
  Doesn’t generate much disagreement
Then “predict then act” provides a powerful approach for managing risk
What will future conditions be?
Under those conditions, what is best near-term decision?
How sensitive is the decision to those conditions?
“Predict Then Act”

## Slide 4: But Traditional Decision Methods Can Fail If Uncertainty Is Deep
In Early 70s, Forecasters Projected U.S. Energy Use
2.0
1.2
.8
.4
0
180
Energy use (1015 Btu per year)
Historical trend continued
1970
1920
1929
1940
1950
1960
1910
1973
1900
1890
20
40
60
80
100
120
140
160
1.6
0
1975 Scenarios
Gross national product (trillions of 1958$)

## Slide 5: But Traditional Decision Methods Can Fail If Uncertainty Is Deep
2.0
1.2
.8
.4
0
180
Energy use (1015 Btu per year)
Historical trend continued
1970
1920
1929
1940
1950
1960
1910
1973
1900
1890
20
40
60
80
100
120
140
160
2000 Actual
1990
1980
1977
1.6
0
1975 Scenarios
Gross national product (trillions of 1958$)
They Were All Wrong About Energy Usage

## Slide 6: Climate Forecasts Reflect Deep Uncertainty
Climate forecasts vary by:
  Climate model (GCM) and model generation,
  GHG emissions forecast,
  Spatial downscaling approach
There is no universally agreed best model, emissions forecast, or method.
Probabilities cannot be reliably assigned to alternative forecasts
Projections used here derive from:
  Last published IPCC assessment (CMIP3)
  In-progress IPCC assessment (CMIP5)
  In-progress innovative UCT downscaling approach

## Slide 7: Multiple Climate Projections for the Orange-Senqu Show T Increasing and P Fluctuating around Mean
Notes: A wide range of available annual average temperature forecasts, shown here for the Volta basin area

## Slide 8: With Similar Patterns When Viewed on a Monthly Basis
Notes: A wide range of available annual average precipitation forecasts, shown here for the Volta basin area

## Slide 9: Traditional Methods Can Backfire in Such Deeply Uncertain Conditions
Uncertainties are underestimated
Competing analyses can contribute to gridlock
Misplaced concreteness can blind decisionmakers to surprise
What will future conditions be?
Under those conditions, what is best near-term decision?
How sensitive is the decision to those conditions?
“Predict Then Act”

## Slide 10: Robust Decision Making (RDM) Works Better Under Deeply Uncertain Conditions by Running the Analysis Backwards
Start with a proposed strategy
Use multiple model runs to identify conditions that best distinguish futures where strategy does and does not meet its goals
Identify steps that can be taken so strategy may succeed over wider range of futures
Proposed strategy
Identify vulnerabilities of this strategy
Develop strategy adaptations to reduce vulnerabilities
“RDM Process”

## Slide 11: RDM Uses Analytics to Facilitate New Conversation with Decision Makers
1. Participatory Scoping
2. System Evaluation across Many Cases
3. Vulnerability Assessment
4. Adaptation Tradeoffs
Dialogue
Analysis
Dialogue and Analysis
Scenarios and
strategies
Outcomes
Vulnerabilities
and leading strategies
Vulnerabilities
Robust
Strategy
New
insights

## Slide 12: RDM Used to Evaluate PIDA Vulnerabilities and Adaptation Options for the Volta River Basin
Volta
River Basin
Notes: Volta River Model
Originally developed by IRD and IUCN
Hosted by Volta Basin Authority
Includes:
Domestic water demand for 22 million people and 10.5 cattle
Major irrigation projects and water storage and hydro facilities
Impacts of climate change

## Slide 13: Preliminary Scoping of Volta River Basin Analysis
Uncertainties (X) | Water Management Strategies (L)
Climate Temperature Precipitation | PIDA+ Baseline
Model (R) | Performance Metrics (M)
WEAP Volta Model | Domestic unmet demand and reliability Irrigation unmet demand and reliability Livestock unmet demand and reliability Hydropower production and firm yield

## Slide 14: PIDA+ Projects Included in the Volta Model
Hydro Power Projects |  | Irrigation Projects
Akosombo | Jambito | Bui Irrigation
Badongo | Juale | Noumbiel Irrigation
Bagre Aval | Koulbi | Pwalugu Irrigation
Bon | Kpong | Sabari Irrigation
Bontioli | Kulpawn | Samendeni Irrigation
Bonvale | Lanka | Nawuni Irrigation
Bui Dam | Noumbiel | Senchi Irrigation
Daboya | Ntereso | 
Gongourou | Pwalugu | 

## Slide 15: WEAP Volta Model Evaluated System Many Times to Understand Ranges of Climate Impacts
Climate projections
(57 projections)
Demand projections (1)
PIDA+ projects
Other adaptation strategies (4)
Domestic water use
Livestock water use
Agricultural water use
Hydropower
Run model for hundreds of futures.
Each future represents one set of assumptions about future climate, demand, and other trends
Other
Uncertainties (later analyses)
Notes: WEAP model…

## Slide 16: PIDA+ Plans Would Moderately Increase Hydropower Production and Significantly Increase Irrigation Demand Under Historical Climate Conditions
(Very dry historical year)

## Slide 17: We Summarize Over Years Using Hydropower Firm Yield and Irrigation Reliability
3,697 GWH
37/41 years =
90.2% reliable
- Historical Climate
- Each dot indicates
results for an individual year
Hydropower Firm Yield =
Minimum yield in all but 5% of years
Irrigation Reliability = Percentage of years in which 90% of irrigation demand is supplied
Reliability Standard

## Slide 18: Performance in the Volta Varies Significantly Across GCM Climate Projections
Historical climate

## Slide 19: Performance in the Volta Varies Significantly Across GCM Climate Projections
(both sectors under-perform)
(irrigation okay, hydro
under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)
Historical climate +
56 climate projections

## Slide 20: Which Future Climate Conditions Would Lead to Under Performance?
(both sectors under-perform)

## Slide 21: We Evaluated Climate Conditions Across Volta River Basin
Upper Basin (Wayen)

## Slide 22: We Evaluated Climate Conditions Across Volta River Basin
Lower Basin (Senchi)

## Slide 23: We Evaluated Climate Conditions Across Volta River Basin
Entire Basin (weighted average)

## Slide 24: Scenario Discovery Techniques Identify Climate Conditions That Lead to Low Performance
Mean annual precipitation < 1,007 mm &
Mean annual temperature > 28.6 deg C
Entire Basin (weighted average)

## Slide 25: The Volta PIDA+ Strategy is Vulnerable to Key Climate Conditions
Vulnerable scenario:
  Mean annual precipitation < 1,007 mm &
  Mean annual temperature > 28.6 deg C
Describes 100% of low performance outcomes(10 of 10)
77% of outcomes are low performance (10 of 13)

## Slide 26: Key Vulnerability Suggests New Adaptation Strategies
Uncertainties (X) | Water Management Strategies (L)
Climate Temperature Precipitation | PIDA+ Baseline Adaptation Strategies Increase irrigation efficiency Increase hydropower capacity Prioritize hydropower
Model (R) | Performance Metrics (M)
WEAP Volta Model | Domestic unmet demand and reliability Irrigation unmet demand and reliability Livestock unmet demand and reliability Hydropower production and firm yield

## Slide 27: Baseline PIDA+ Strategy Performance Acros 57 Climate Projections
(both sectors under-perform)
(irrigation okay, hydro
under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)

## Slide 28: Irrigation Efficiency Improves Irrigation Reliability for Dry Projections
(both sectors under-perform)
(irrigation okay, hydro
under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)

## Slide 29: Increased Hydropower Capacity Increases Firm Yield for Wet Projections
(both sectors under-perform)
(irrigation okay, hydro
under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)

## Slide 30: Increased Hydropower Priority Increases Firm Yield but Decreasing Irrigation Reliability
(both sectors under-perform)
(irrigation okay, hydro
under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)

## Slide 31: Increased Irrigation Efficiency and Increasing Hydropower Priority Strikes Alternative Balance
(both sectors under-perform)
(irrigation okay, hydro
under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)

## Slide 32: New Strategies Decrease Some Climate Change Vulnerability with Tradeoffs

## Slide 33: Alternative Strategies Decrease Some Climate Change Vulnerability with Tradeoffs

## Slide 34: Next Step for Volta River Basin Analysis
Examine performance in greater detail
  Regionally and by facility
Develop and evaluate additional adaptation strategies
Hold workshop with stakeholders to discuss outcomes and key tradeoffs

## Slide 35: Robustness Analysis for Energy
Energy model development is underway
We are developing the robustness analysis structure and components
  Beginning with the SAPP

## Slide 36: Energy Modeling Analyzes the PIDA+ Projects
Project name | North–South Power Transmission Corridor | Mphamda-Nkuwa | Lesotho HWP phase II hydropower component
Description | 8,000 km line from Egypt through Sudan, South Sudan, Ethiopia, Kenya, Malawi, Mozambique, Zambia, Zimbabwe to South Africa | Hydroelectric power plant with a capacity of 1,500 MW for export on the SAPP market | Hydropower programme for power supply to Lesotho and power export to South Africa
Power Generation Type | Transmission | Hydro | Hydro
Country | Kenya, Ethiopia, Tanzania, Malawi, Mozambique, Zambia, Zimbabwe, South Africa | Mozambique | ?
Budget ($million) | 6000 | 2400 | 800
Phase | feasibility/needs assessment | feasibility/needs assessment | feasibility/needs assessment
Basin | Nile . Zambezi | Mozambique, Zambezi basin | Orange-Senqu River Basin
Power Pool | Southern African Power Pool | Southern African Power Pool | Southern African Power Pool
Notes: Remove, mark to give a new one.

## Slide 37: Energy Robustness Analysis
Energy Model
C1
C2
C3
C4
Water Model
Participatory Scoping
System Evaluation Across Cases
Vulnerability Assessment
Adaptation Tradeoffs
Robust Strategies
Vulnerabilities and leading strategies
RDM

## Slide 38: RDM Structure for the Energy Analysis
Uncertain Factors (X) | Decision Variables (L)
Future Climate Fuel costs Energy demand Cost and performance of energy systems Energy security Greenhouse gas policies | Energy investment in PIDA+ (baseline strategy) Adaptive responses Revised investment timing Enhanced regional integration across power pools Enhanced energy institutions (cost recovery, energy pricing)
Power Pool Models (R) | Objective Variables (M)
Aggregated country-level OSeMOSYS models of power pools (drawing on WEAP analysis) | Financial metrics (cost of power) Energy supply Unserved power demand

## Slide 39: Want to Integrate the Water and Energy Analysis Where Feasible
Energy systems rely on water resources
  Hydropower production
  Cooling for many types of power plants
  Irrigation for biofuels
Water management depends on energy systems
  Energy demand for hydropower
  Withdrawals for cooling
We will address this feedback cycle

## Slide 40: Step 1 Energy Modeling Influenced by Water, Step 2 Considers Energy Impacts on Water
Step 1: Power pool/basin studies
  Unidirectional: WEAP informs energy model
Step 2: Project-level studies
  One complete iteration of water-energy feedback
WEAP
Energy model
Optimal investment
WEAP
Energy model
Optimal investment
Water Demand
Re-run WEAP with energy-related water needs—if shortages, re-run energy model

## Slide 41: We Have Begun an RDM Analysis for the Orange River Basin

## Slide 42: Preliminary Scoping of Orange River Basin Analysis
Uncertainties (X) | Water Management Strategies (L)
Climate Temperature Precipitation | PIDA+ Baseline
Model (R) | Performance Metrics (M)
WEAP Orange Model | Domestic unmet demand and reliability Irrigation unmet demand and reliability Hydropower production and firm yield

## Slide 43: We Evaluated Climate Conditions Across Orange River Basin
Lower Basin (D31)

## Slide 44: We Evaluated Climate Conditions Across Orange River Basin
Upper Basin (D11A-F)

## Slide 45: We Evaluated Climate Conditions Across Orange River Basin
Basin Average
Scenario discovery techniques next identify climate conditions that lead to low performance

## Slide 46: Most Scenarios Show Higher Firm Hydropower Yield and Half Show Higher Irrigation Reliability
13/56 scenarios show lead to low firm hydropower yield and/or low irrigation reliability
(both
sectors
under-
perform)
(irrigation okay,
hydro under-performs)
(hydro okay, irrigation
under-performs)
(both sectors okay)

## Slide 47: Which Future Climate Conditions Would Lead to Under Performance?
(both sectors under-perform)