## Slide 1: E: Track II Project level analyses
Robert Lempert, RAND

## Slide 2: Project Has Two Tracks
Analyses consistent across basins and power pools (Track I)
Water
Energy

## Slide 3: Project Has Two Tracks
Analyses consistent across basins and power pools (Track I)
Project level analyses (Track II)
  Conduct five case studies, each focusing on a specific project
  Goals of project-level analyses:
    Benefit managers of the projects studied
    Enrich response options analysis in basin-level studies
    Develop widely usable tools Bank and others can use

## Slide 4: Initial Case Study Considers Malawi’s Lower Fufu Hydro-Power Project
Project basics:
  Hydropower (90 MW)
  Estimated cost: $600M
Performance metrics
  Firm power (MWh / yr)
  Levelized energy cost (US$/ KWh)

## Slide 5: Analysis Builds on Data in 1995 Prefeasibility Report
Estimates from 1995 report:
  Capital cost: $118.75M
  Annual fixed operating costs: $1.78M/year (roughly 1.5% of capital cost)

## Slide 6: Analysis Will Stress-Test Project Across Wide Range of Plausible Futures
Analytic Approach
  Use hydrological and financial model to evaluate performance metrics under many future conditions (climate and other uncertain variables)
  Identify cases where performance is unacceptably low
  Consider design choices that can reduce vulnerability in as many cases as possible
Design choices include
  Plant capacity
  Height of dams
  Diameter of supply tunnels

## Slide 7: Built Simple Analytic Framework for Evaluating the Robustness of Lower Fufu Hydropower Project
WEAP model of hydro project
Excel-based hydropower
project cost model
By project specification
and climate and other
assumptions:
Firm yield
Unit costs
Alternative hydropower
project specifications
Which project
specifications
are most robust
in terms of firm
yields and energy
costs?
Climate change
hydrologies
Capital costs
O&M costs
Other assumptions
Financial and other
assumptions
Excel model of hydro project costs

## Slide 8: Simulated Hydropower Production Over Time: Historical Climate
56 GCM Projections
+ Historical
Historical

## Slide 9: Simulated Hydropower Production Over Time: 56 Climate Projections
56 GCM Projections
+ Historical
Historical

## Slide 10: Average Hydropower Production Varies Across Climate Projections
56 GCM Projections
+ Historical
Average Annual Hydropower
Production Range:
  530 – 644 GWh

## Slide 11: With Current Project Configuration Hydropower Unit Costs Vary Across Climate Projections
Annual costs assuming 5% annual interest rate and 40-year payback period:
  $12.4M (capital costs) + $1.3M (O&M costs) = $13.6M/year
Annual production range:
  530 – 644 GWh
Range in Energy costs:
  0.021~ 0.026 $/kWh

## Slide 12: Next Steps to Consider on Fufu Case Studies
Additional uncertainties
  Hydraulic efficiency (nominal is 88%)
  Infrastructure cost parameters
  Financial terms
  Larger instream flow requirements (reduce diversion potential)
  Demand for power at required price
Alternative project designs
  Larger and smaller supply tunnels
  Larger and smaller generating capacity
  Alternative energy sources

## Slide 13: Some Criteria for Choosing Next Four Case Studies
Project in one of the seven basins considered in Track I analyses
Project between pre-feasibility and feasibility study phases
Sufficient data in pre-feasibility study to inform the simple, excel-based model
Interest among relevant decision makers